## Slide 1: Kaiba Corp. EE Capstone 2014
Alyanna Castillo
Patrick Ma
Ryan McDaniel

## Slide 2: Project vision
Problems:
  Design a complete embedded capstone
  Must have at least 60% hardware components
  Children looking for entertainment
  Teach children
Our solution:
  Build an RFID compatible learning device
  Plays educational and entertainment games

## Slide 3: Capstone Deliverables
One working prototype system
Documentation
Another working prototype system (hopefully)

## Slide 4: Presentation Flyover
Vision & project Summary
Deliverables
Define requirements and specifications
High level implementation details
  Describe HW/SW
  System flow
  General game play
Issues encountered
Latest Results
Current project status
Comments

## Slide 5: System Requirements
Read multiple RFID tags
Physically react to placed cards
Display data on cards /or players
Communicate wirelessly on multiple frequencies
Interact with user and respond to user input
Track game progress and display relevant game information
Manipulate game data
Maintain a database of cards
Run fast enough to provide “real-time” user experience

## Slide 6: Specifications
Operate under normal household conditions
Compliant with EIA-232, ISO15693, I2C, FCC Part 15.A,C standards

## Slide 7: Our Idea: Hardware

## Slide 8: Hardware summary
Components (single system):
    RFID Reader/Writer
    XBee 802.11.4
    (2) GAL22V10
    (2) PIC18F46K22
    (2) 2k 8-bit SRAM
    16-key keypad
    4” LCD
    3.3v regulator
    (4) switches
    H-bridge
    Linear servo
    20MHz Crystal Oscillator
    CMOS hex buffer (non-inverting)
    (3) RGB LEDs

## Slide 9: Schematic

## Slide 10: Software functions

## Slide 11: State machines
Basic system flow
Generic game flow

## Slide 12: Issues Encountered
Lack of memory + pins
  Solution: switched to larger chip from same family
    PIC18F46K22
    36 GPIO pins
  Solution: use a two-level system (frontend + backend)
UART ISR overflow
  Occurred when reading RFID tags
  Limited to specific functions
  Root cause:
    excessive context switch lag time
  Solution:
    remove function calls within ISR
    Instruct Compiler to not save data

## Slide 13: Status
Most hardware modules tested/working
Integrating software drivers with scheduler
Current game idea?

## Slide 14: Future work
Implement UX reaction
Integrate to scheduler
XBee / intersystem comm
Game loading software